## Slide 1
Prepping for Climate Change: Quantifying Outdoor Water Savings as a Function of Weather
October 14, 2020
Miguel A. Morales, PhD, EIT

## Slide 2: City of Austin, Texas
Serves a population of 1.1M
  Projected to quadruple in next 100 years
Draws water from the Colorado River into three regional water treatment plants (combined capacity of 335 MGD)
Located in Central Texas between the deserts of the SW and the more humid SE
  Long, hot summers – short, mild winters
  Annual average of 34” of rain, wettest during spring and fall

## Slide 3: Weather Variables
Month | Kc
1 | 0.67
2 | 0.56
3 | 0.46
4 | 0.46
5 | 0.45
6 | 0.46
7 | 0.49
8 | 0.58
9 | 0.74
10 | 0.81
11 | 0.91
12 | 0.89
Hourly weather data obtained from Camp Mabry
  NOAA Local Climatological Data (LCD) station
Reference evapotranspiration (ETo)
  Hourly temperature, relative humidity, atmospheric pressure, and wind speed used to calculate daily ETo via the Penman-Monteith method with the Hargreaves approximation for solar radiation
  Aggregated up to calendar months & calibrated to local conditions and irrigation patterns using billing data
    Crop coefficients (Kc) to estimate crop evapotranspiration (ETc)
Hourly precipitation aggregated to calendar months

## Slide 4: Historical ETo (1949-2019)
Chart: 
| Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep
FY 2020 | 4.2985 | 2.4781 | 2.2283 | 2.3715 | 2.7663 | 4.0271 | 5.0282 | 6.4549 | 6.2807 | 7.5293

## Slide 5: Historical Precip. (1949-2019)
Chart: 
| Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep
FY 2020 | 2.96 | 0.63 | 0.83 | 1.63 | 2.2 | 4.01 | 2.86 | 6.26 | 2.66 | 0.65

## Slide 6: GPCD & Weather
Chart: Fiscal Year
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
wet | 159.4907 | 153.4598 | 149.2981 | 144.9828 | 140.4938 | 129.494 | 123.8595 | 117.8475 | 114.234 | 111.6462 | 110.2611 | 110.1162 | 108.841 | 106.0108 | 103.0515
Dry/Wet 80% Confidence Interval | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923
Dry/Wet Weather Band | 32.9214 | 32.9214 | 32.9214 | 32.9214 | 32.9214 | 32.9214 | 32.9214 | 32.9214 | 32.9214 | 32.9214 | 32.9214 | 32.9214 | 32.9214 | 32.9214 | 32.9214
Dry CI | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923 | 4.3923
Actual Avg. GPCD | 175.9456 | 190.257 | 150.5603 | 169.8073 | 167.4405 | 137.0819 | 162.2453 | 141.9536 | 135.5115 | 124.5247 | 121.8689 | 121.2547 | 125.6357 | 125.906 | 120.1788
Modeled Avg. Weather | 179.8459 | 173.815 | 169.6533 | 165.3381 | 160.8491 | 149.8493 | 144.2147 | 138.2028 | 134.5893 | 132.0014 | 130.6163 | 130.4715 | 129.1962 | 126.366 | 123.4067

## Slide 7: Annual Flow of Colorado River @ Austin
Austin Water – Water Forward – Integrated Water Resources Plan

## Slide 8: Palmer Drought Severity Index for Texas
NOAA National Centers for Environmental information, Climate at a Glance: Statewide Time Series, published August 2020 at https://www.ncdc.noaa.gov/cag/

## Slide 9: Foreseen Impact of Climate Change
Rising temperatures and evaporation rates are forecast to accelerate the hydrologic cycle and increase the intensity of heavy precipitation and severity of droughts
University of Birmingham, Brigham Young University, and Michigan State University
Heightened tradeoff between water supply and flood protection

## Slide 10: Adjusting Conservation Savings Rates
Not enough to focus on average savings rates
Important to understand savings when they matter most
  Peak days – drive infrastructure expansion
  Droughts – water supplies most taxed
Jack Newton
LCRA

## Slide 11: Capacity-Based Rainwater Harvesting Rebate (RWH)
Started in 2010
Offers rebate based on rainwater storage capacity
  $0.50/gal capacity for non-pressurized systems
  $1.00/gal capacity for pressurized systems
From 2010-2018:
  2,555 rebates given to 2,395 customers
  $980k in rebates for $3.33M spent by customers
  1.64 million gallons of rainwater storage capacity

## Slide 12: Single-Family Residential (SFR) Participation
Type | Total Customers | Total Rebates | Avg. Conservation Activities per Customer | Avg. Rebate Amount | Avg. Amount Spent by Customer | Avg. Rainwater Storage Capacity (gal)
Non-Pressurized | 2,223 | 2,371 | 1.93 | $197 | $707 | 389
Pressurized | 173 | 176 | 1.77 | $3,127 | $10,124 | 4,431
Total | 2,396 | 2,547 | 1.92 | $409 | $1,387 | 681

## Slide 13: Watering Restrictions
Twice-a-week watering restrictions implemented in May 2008 in response to historic drought
Alternated between once-a-week, twice-a-week, and no restrictions in subsequent years
Once-a-week restrictions made permanent in September of 2012

## Slide 14: Data Filters to Isolate RWH Effect
Post-2012 billing (remove transition into permanent watering restrictions)
Continuous billing (remove homes that were unoccupied for extended periods of time)
Same customer throughout (attempt to isolate agent and associated behavioral components)
No other conservation activity (attempt to further isolate impact of RWH)
Control group with same filters (attempt to isolate effect of passive conservation)
  Based on SFR from same Census Blocks which did not participate in RWH or any other conservation activity
Billing data rectified or adjusted to calendar months

## Slide 15: Non-Pressurized RWH
Chart: GPCD
 | Participants | Control
Parcels | 275 | 4,236
Avg. People per Home | 2.49 | 2.49
Year Built | 1976 | 1975
Building Area (sf) | 1,946 | 1,896
Pervious Area (sf) | 8,655 | 7,991
Appraised Value | $462,439 | $456,402

## Slide 16: Non-Pressurized RWH
Time series regression on the aggregate does not show statistically significant water demand reduction associated with non-pressurized rainwater harvesting
Chart: Participants GPCD / Control GPCD

## Slide 17: Non-Pressurized RWH
Chart: ETc (in/d)
| 5.1792107416294239E-2 | 6.9068854685869693E-2 | 7.3507572150030245E-2 | 7.6419676470310977E-2 | 9.1441460968548688E-2 | 0.11024149968851336 | 0.11584538831866675 | 0.13537502860265069 | 0.12887392261971914 | 9.8908748133055377E-2 | 7.1338242806594634E-2 | 5.1936297891599835E-2
Participants Pre-RWH (2013) | 59.2273 | 62.5086 | 72.9598 | 74.1006 | 79.3253 | 103.1962 | 111.3248 | 118.3005 | 96.6445 | 63.4243 | 54.7709 | 52.078 | 52.516 | 54.3297 | 60.363 | 72.0823 | 75.0265 | 75.7566 | 92.4504 | 109.1191 | 82.7392 | 65.9528 | 56.0561 | 51.0271
Participants Post-RWH (2019) | 43.6188 | 44.3075 | 52.0238 | 52.5743 | 52.194 | 61.7173 | 89.9907 | 117.6162 | 105.0205 | 74.0715 | 51.6717 | 48.6381
Control Pre-RWH (2013) | 76.8538 | 72.574 | 88.623 | 89.2852 | 97.5805 | 118.1895 | 133.6321 | 136.456 | 109.8693 | 79.0407 | 68.1628 | 69.1548
Control Post-RWH (2019) | 55.5387 | 51.1722 | 66.187 | 64.4534 | 67.1173 | 76.1103 | 109.4395 | 140.6302 | 124.5177 | 94.6298 | 64.8912 | 61.5355

## Slide 18: Non-Pressurized RWH
Weather Condition | ETc (in/d) | Participants (GPCD) |  |  | Control (GPCD) |  |  | Participants / Control |  | 
 |  | Pre-RWH | Post-RWH | % Diff. | Pre-RWH | Post-RWH | % Diff. | Pre-RWH | Post-RWH | % Diff.
Avg. Winter Min | 0.05 | 53 | 43 | -19.9% | 68 | 53 | -21.5% | 78.4% | 79.9% | 1.6%
Avg. Annual | 0.09 | 73 | 61 | -16.7% | 89 | 76 | -15.5% | 82.1% | 80.9% | -1.3%
Avg. Summer Max | 0.13 | 112 | 98 | -12.2% | 128 | 120 | -6.8% | 87.3% | 82.2% | -5.5%

## Slide 19: Pressurized RWH
Chart: GPCD
 | Participants | Control
Parcels | 16 | 256
Avg. People per Home | 2.42 | 2.42
Year Built | 1965 | 1968
Building Area (sf) | 2,546 | 2,293
Pervious Area (sf) | 14,416 | 11,768
Appraised Value | $788,225 | $685,101

## Slide 20: Pressurized RWH
Time series regression on the aggregate again does not show statistically significant change in water demand associated with pressurized rainwater harvesting, though less so!
Chart: Participants GPCD / Control GPCD

## Slide 21: Pressurized RWH
Chart: ETc (in/d)
| 5.1792107416294239E-2 | 6.9068854685869693E-2 | 7.3507572150030245E-2 | 7.6419676470310977E-2 | 9.1441460968548688E-2 | 0.11024149968851336 | 0.11584538831866675 | 0.13537502860265069 | 0.12887392261971914 | 9.8908748133055377E-2 | 7.1338242806594634E-2 | 5.1936297891599835E-2
Participants Pre-RWH (2013) | 63.2475 | 74.0251 | 98.0637 | 93.862 | 99.5551 | 148.5675 | 130.9427 | 136.1524 | 120.9383 | 69.9336 | 62.1958 | 57.0413
Participants Post-RWH (2019) | 49.1625 | 56.8795 | 64.3918 | 68.2484 | 60.4741 | 96.8719 | 148.3028 | 187.9923 | 196.7253 | 118.5795 | 64.7805 | 66.6728
Control Pre-RWH (2013) | 93.9515 | 95.7528 | 121.5169 | 117.047 | 122.8332 | 150.7147 | 165.4021 | 186.2143 | 140.8507 | 86.9111 | 78.8375 | 77.3745
Control Post-RWH (2019) | 62.185 | 56.776 | 78.0039 | 78.2877 | 79.6037 | 95.271 | 153.1272 | 201.8447 | 179.0419 | 127.7831 | 76.9067 | 72.9085

## Slide 22: Pressurized RWH
Weather Condition | ETc (in/d) | Participants (GPCD) |  |  | Control (GPCD) |  |  | Participants / Control |  | 
 |  | Pre-RWH | Post-RWH | % Diff. | Pre-RWH | Post-RWH | % Diff. | Pre-RWH | Post-RWH | % Diff.
Avg. Winter Min | 0.05 | 61 | 51 | -17.6% | 82 | 60 | -27.0% | 74.8% | 84.5% | 9.4%
Avg. Annual | 0.09 | 88 | 85 | -3.3% | 111 | 94 | -15.6% | 78.9% | 90.4% | 12.3%
Avg. Summer Max | 0.13 | 140 | 168 | 19.6% | 166 | 170 | 2.3% | 84.6% | 99.0% | 17.3%

## Slide 23: Conclusions & Future Work
Important to understand the impact of weather on water demand to compare usage patterns and evaluate conservation savings when they matter most
Test case highlights the weather dependency of outdoor water savings and offers some interesting results:
  Non-pressurized RWH: slight increase in usage in cooler months, larger decrease in usage in hotter months
  Pressurized RWH: increased usage throughout the year, though much more so in hotter months (creating new demand?)
Improve sample sizes and further explore panel regression
Incorporate likely climate change scenarios into long-term planning

## Slide 24
Contact:
Miguel.Morales@austintexas.gov
512-974-3545